## Slide 1: Hazardous Waste Generator Improvement Rule
For:
Elkhart chamber environmental committee
Prepared by:
Last Updated: September 25, 2018

## Slide 2: Table of Contents
RCRA Overview
  History of Rule
  Generator Universe
  Goals of the Final Rule – per the EPA
Rule Provisions
  Reorganization
  Waste Determinations
  Waste Counting
  Consolidation of waste at LQG
  Episodic Event
  Marking and Labeling
  Satellite Accumulation Areas
  SQG Re-notification
  Emergency Planning and Preparedness
  50 – foot waiver
  Reporting and Recordkeeping
  Closure

## Slide 3: Rule Process and Schedule
Rule Signed on October 28, 2016
Publication in Federal Register – November 28, 2016
Effective Date – May 30, 2017
Authorized states go through adoptions and authorization process for more stringent
  July 1, 2018 or July 1, 2019 if state law change is needed
  Indiana requires state law change – expected Q1 2019
Authorized states may choose to pick up less stringent
  Expecting Indiana to adopt HWGIR in entirety

## Slide 4: The Universe of Waste
Not a Waste
Solid Waste
Hazardous
Waste

## Slide 5: Definition of a Solid Waste
Abandoned
Recycled
Inherently Waste Like

## Slide 6: Definition of Hazardous Waste
Solid Wastes are Hazardous Wastes if:
It is a Characteristic Waste:
Ignitable
Corrosive
Reactive
Toxic
It is a Listed Waste

## Slide 7: Types of Generators
Generator Status | Thresholds (per month) | Total HW Generated (tons) * | Percent of Total Waste Generated
VSQGs | <220 lbs | 46,000 – 148,000 | <1%
SQGs | 220 – 2,200 lbs | 66,000 – 141,000 | <1%
LQGs | <2,200 lbs | 35.2 Million | 99%

## Slide 8: Goals of the Rule
Over 60 changes were made to the HW rule that:
Reorganize the regulations to make them more user friendly
Provide greater flexibility – cost effective management
  Episodic events
  VSQG  LQG consolidation
Filling in gaps to strengthen environmental protection
Clarify certain components and address ambiguities

## Slide 9: Stringency of Final Rule
More stringent
SQG re-notification
Identifying hazards and labeling
Notification of closure
Biennial reporting for whole year, not just months was an LQG
Biennial reporting for recyclers who don’t store prior to recycling
Quick reference guide for contingency plans
Less Stringent
VSQG consolidation
Episodic generation
Waiver from 50-foot rule

## Slide 10: Reorganization
Provision | Existing Citation | Final Citation
Generator Category Determination | 261.5(c)-(e) | 262.13
VSQG Provisions | 261.5(a), (b), (f)-(g) | 262.14
Satellite Accumulation | 262.43(c) | 262.15
SQG Provisions | 262.34(d)-(f) | 262.16
LQG Provisions | 262.34(a), (b), (g)-(i), (m) | 262.17

## Slide 11: Hazardous Waste Determination 262.11(a)
The hazardous waste determination for each solid waste must be made at the point of waste generation…
RCRA Statute is clear – the term “hazardous waste generation” means the act or process of producing hazardous waste.
Why at the point of generation?
To ensure:
Proper waste identification
Proper handling and management from “cradle to grave”
Strengthening Environmental Protection

## Slide 12: Hazardous Waste Determination 262.11(a)
The hazardous waste determination for each solid waste must be made at the point of waste generation, before any dilution, mixing or other alteration of the waste occurs…
EPA added this language to state their existing interpretation that you must characterize your waste before dilution, mixing or alteration
Alteration of waste: May change waste properties and subsequent handling
  Example: allow volatile organics volatilize from an uncovered container
Strengthening Environmental Protection

## Slide 13: Hazardous Waste Determination 262.11(a)
The hazardous waste determination for each solid waste must be made at the point of waste generation, before any dilution, mixing or other alteration of the waste occurs, and at any time in the course of its management that it has, or may have, changed its properties as a result of exposure to the environment or other factors that may change the properties of the waste such that the RCRA classification of the waste may change
Generators must understand chemistry of their wastes
A SW determined to be non-hazardous at the POG may change while being managed on site through exposure to environment
Note: the opposite may be true
Does this mean you need to monitor your waste 24/7?
Strengthening Environmental Protection

## Slide 14: Hazardous Waste Counting
A hazardous waste generator has always had to count their hazardous waste to determine their category
The regulations did not present requirements about determining generator categories in a clear and succinct way
New § 262.13 clarifies the process for a generator to determine its generator category each calendar month
This provision also discusses how mixing of hazardous waste with non-hazardous waste impacts generator category.
Clarifying Regulations

## Slide 15: Mixing – What Changed?
Reorganization distinguished VSQGs mixing requirements from those for SQGs and LQGs
Clarified VSQGs mixing solid waste with hazardous wastes and generating characteristic waste must count that waste towards their generator category for that month
Made clear that SQGs and LQGs mixing solid wastes with hazardous wastes are subject to certain restrictions and requirements.
Clarifying Regulations

## Slide 16: VSQG Mixing
Clarifies that a VSQG mixing hazardous waste with solid waste can remain subject to VSQG requirements even though the mixture may exceed the VSQG quantity limits as long as the mixture does not exhibit one or more of the characteristics of a hazardous waste.
If the resultant mixture does exhibit a hazardous waste characteristic, the mixture is a newly generated hazardous waste.
Clarifying Regulations

## Slide 17: SQGs and LQGs Mixing
Mixtures of hazardous waste and solid waste at SQGs and LQGs are subject to:
  The mixture rule in §§ 261.3(a)(2)(iv), (b)(2) and (3), and (g)(2)(i); 
  The prohibition of dilution rule at § 268.3(a);
  The land disposal restriction requirements of § 268.40 if a characteristic hazardous waste is mixed with a solid waste so that it no longer exhibits the hazardous characteristic; and
  The hazardous waste determination requirement at § 262.11
Clarifying Regulations

## Slide 18: Mixing vs Dilution
Generators can’t dilute their hazardous wastes unless it provides a useful and effective contribution (i.e., possess a unique property to remove the hazardous characteristic from the hazardous waste instead of merely diluting it).

## Slide 19: Mixing: Why the Changes?
Changes are designed to clarify the language that was found at § 261.5(h) and (i) which addressed the mixing of hazardous waste and nonhazardous waste by a VSQG
The language specifically addressed how the regulations apply when VSQG hazardous waste is mixed with nonhazardous solid waste and the resulting combination exceeds the VSQG quantity limits.
The previous regulations also did not specifically discuss SQGs and LQGs mixing solid wastes with hazardous wastes in the generator provisions.

## Slide 20: Waste Consolidation
What was the problem with the old rule?
Some companies would like to be able to consolidate wastes from their own VSQG sites for more efficient shipping and hazardous waste management
  Reduces liability for company as a whole by ensuring proper management of hazardous waste
  Sending to a RCRA-designated facility is the most environmentally sound option
  Previously an LQG needed a RCRA permit to receive VSQG wastes
Enhancing Generator Flexibility

## Slide 21: VSQG Consolidation at LQGs
New Consolidation Provision
Consolidate waste at an LQG under the control of the same person:
  Control – means the power to direct policies at the facility
VSQG standards
  Marks and labels waste containers with “Hazardous Waste” and the hazards
No hazardous waste manifest is required and hazardous waste transporters do not have to be used
Enhancing Generator Flexibility
Notes: Person – means an individual, trust, firm, joint stock company, Federal Agency, corporation (including a government corporation), partnership, association, State, municipality, commission, political subdivision of a State, or any interstate body

## Slide 22: VSQG Consolidation at LQGs
LQG Standards
Notifies state on Site ID Form that it is participating in this activity and identifies which VSQGs are participating
Recordkeeping for each shipment – normal business records
Adds accumulation start date to VSQG HW labels when arrives at LQG
Manages consolidated waste as LQG hazardous waste
Reports in Biennial Report – there will be a different source code (G51) for the VSQG consolidated waste to distinguish from the LQG’s own generated waste
EPA did not extend this provision to allow SQGs to consolidate VSQG HW, but an SQG can participate if they notify and act as an LQG (meeting all LQG standards including getting the VSQG HW off-site in 90 days)
Enhancing Generator Flexibility

## Slide 23: VSQG Consolidation at LQGs
FAQs about Consolidation Provision
When does the 90-day clock start for VSQG consolidated waste?
  When the VSQG waste gets to the LQG, the 90-day clock to accumulate the waste starts
Is there any accumulation limit for how much waste can be consolidated at an LQG?
  No, there is no overall accumulation limit but the waste must be sent off-site to a RCRA TSDF or recycler within 90 days
Does the LQG add the VSQG waste to its annual generation amount?
  The LQG would report both its own generated waste and the waste consolidated from its VSQGs on the Biennial Report. However, there is a different source code (G51) for the VSQG waste so they can distinguish between their own HW and the consolidated waste
Enhancing Generator Flexibility

## Slide 24: VSQG Consolidation at LQGs
FAQs about Consolidation Provision
When transporting the waste from the VSQG to the LQG, what requirements must be met?
  There are no specific requirements other than applicable DOT requirements
Is there a quantity limit for shipments from the VSQG
  No, but the VSQG must stay within its own accumulation limit
Can VSQG and LQG be in different states?
  Yes, if both states have adopted the consolidation provision. If the HW is transported through other states, the generator should check with the transit state to see if they can pass through
Enhancing Generator Flexibility

## Slide 25: VSQG Consolidation at LQGs
FAQs about Consolidation Provision
What marking and labeling should be on the containers?
  At the VSQG, the words “Hazardous Waste” and the hazards
  At the LQG, the words “Hazardous Waste”, the hazards and the accumulation start date
Can the LQG consolidate the VSQG HQ within the same container with their own LQG HW
  Yes, if the waste is compatible. The LQG would need to use the earlier accumulation start date on the combined HW to determine how long the combined HW can remain on-site.
Enhancing Generator Flexibility

## Slide 26: VSQG Consolidation at LQGs
FAQs about Consolidation Provision
Does the LQG have to retain shipping records
  Yes, the records would have to be kept for three years and must include:
    The name, address, and contact info for the VSQG, and
    A description of the waste received, including the quantity and date the VSQG waste was received
    This does not need to be on a manifest.
Enhancing Generator Flexibility

## Slide 27: Episodic Event
Current RCRA rule lacks flexibility to address “episodic” events
Planned event (i.e. tank cleanouts)
Unplanned events (i.e. production upsets, spills, acts of nature)
Currently, generators must comply with LQG/SQG regulations for when not regular generators of higher levels of hazardous waste
Enhancing Generator Flexibility

## Slide 28: Episodic Event
Final Provision allows generators to maintain existing category provided they comply with streamlined set of requirements
Applies to VSQG and SQG
One event per calendar year with ability to petition for 2nd
  If first event is planned, the 2nd must be unplanned and vice versa
Notify EPA or state at least 30 days prior to initiating a planned episodic event
Notify EPA or state within 72 hours after an unplanned event
Enhancing Generator Flexibility

## Slide 29: Episodic Event
Duration of an Episodic Event
First day of the episodic event is the first day of waste generation.
Episodic event can last 60 days
All hazardous waste must be shipped off site by the end of 60 days
If the generator does not know if the event is going to be episodic, EPA recommends notification.
May complete multiple projects during the time limit
Enhancing Generator Flexibility

## Slide 30: Episodic Event
Streamlined requirements for VSQGs
Obtain RCRA ID Number
Use hazardous waste manifest and transporter to designated facility
Manage in a manner that minimizes possibility of an accident or release
Label episodic waste containers
“Episodic Hazardous Waste”
Indication of hazards of the contents
Date the episodic event began
Identify an emergency coordinator
Maintain records associated with episodic event
Enhancing Generator Flexibility

## Slide 31: Episodic Event
SQGs need only comply with existing SQG regulations and maintain records associated with the episodic event
Enhancing Generator Flexibility

## Slide 32: Episodic Event
Recordkeeping:
Records must be maintained for 3 years from completion of each event
Elements:
Beginning and end date of episodic event (notification)
Description of episodic event (notification)
Types of hazardous wastes generated
How the wastes were managed at TSDF or recycler (manifest)
Name of hazardous waste transporters (manifest)
Approval letter if approved for 2nd event
Quantities of hazardous waste generated (manifest)
Enhancing Generator Flexibility

## Slide 33: Episodic Event
Petition for 2nd event
Made in writing
Include reason for the event, estimated amount, how the waste will be managed, estimated length of episodic event and information about previous event in the same calendar year
Planned event
Petition submitted to EPA or state 30 or more days prior to event
Unplanned event
Notify EPA or state within 72 hours by phone or email, followed by submittal of form 8700-12 and indication this is second event
Enhancing Generator Flexibility

## Slide 34: Marking and Labeling
Current rule do not require generators to identify and indicate the hazardous of the wastes accumulated
Resulted in failure to communicate risks
Can impact workers, handlers, emergency responders and visitors
Strengthening Environmental Protection

## Slide 35: Marking and Labeling
Areas affected
Satellite Accumulation Areas
Central Accumulation Areas
Transfer facilities consolidating hazardous wastes
Generator container and tanks storage areas at TSDF
Strengthening Environmental Protection

## Slide 36: Marking and Labeling
Final Rule
Containers and tanks must indicate the hazards of the contents
May use a number of methods
DOT HazComm
OSHA hazard statement or pictogram
NFPA chemical hazards label
RCRA characteristic
Note: the labels are not required to include the identify of the contents (as proposed)
Strengthening Environmental Protection

## Slide 37: Marking and Labeling
Examples
Strengthening Environmental Protection

## Slide 38: Marking and Labeling
Some clarifications:
Labeling should occur at the initial point of generation
Containers with small containers can mark the outer container or attache a tag
Wastes in a container already marked (e.g. a commercial products in its original container), must only mark “Hazardous Waste”
Strengthening Environmental Protection

## Slide 39: Satellite Accumulation Areas
Some clarifications:
Explicitly require incompatible wastes not be mixed
Allow containers to be open temporarily under limited circumstances
Provide maximum weight and volume for acute hazardous waste
Explicitly clarified “three days” is three consecutive calendar days (not operating days)
Rescinded memo allowing reactive hazardous waste to be stored away from point of generation
  If that hazardous, must go directly to CAA
Make marking and labeling consistent with CAA
Strengthening Environmental Protection, Enhancing Generator Flexibility, Clarifying Regulations

## Slide 40: SQG Re-notification
Final Rule
Requires SQGs to re-notify ever 4 years unless states have more frequent re-notification requirements
  Annual already for Indiana
Electronic reporting an option
Compliance date is delayed until 2021 to give some states time to update reporting platforms
Strengthening Environmental Protection

## Slide 41: Emergency Preparedness and Planning
Coordination with Emergency Responders
Previous regulation
Required generator to attempt to make arrangements with local emergency responders
No requirement to document arrangements (only that local emergency responded declined request)
Final Rule
Generators must document they have attempted to make arrangements
No specific form or type of documentation
Strengthening Environmental Protection

## Slide 42: Emergency Preparedness and Planning
Contingency Plan Quick Reference Guide
Problem
Contingency Plans are required to be submitted and are lengthy
Emergency responders want quick access to key information
Final Rule
Requires new LQGs to submit contingency plans with a Quick Reference Guide
Requires existing LQGs to include Quick Reference Guide when they otherwise update their contingency plan
Strengthening Environmental Protection

## Slide 43: Emergency Preparedness and Planning
Contents of Contingency Plan Quick Reference Guide
Type/names of hazardous waste and associated hazards
Estimated maximum amounts of hazardous wastes
Hazardous wastes requiring unique treatment
Map showing where hazardous wastes are generated, accumulated or treated
Map of facility and surroundings to identify routs of access and evacuation
Location of water supply
Identification of on-site notification systems
Name of emergency coordinator(s) or listed staffed positions(s) and 24/7 emergency telephone number(s)
Strengthening Environmental Protection

## Slide 44: Waiver to 50-Foot Requirement
Problem
Generator regulations require that containers with ignitable or reactive wastes be located at least 50 feet from the facility’s property line
Final Rule
Allows LQGs to approach the fire marshal to apply for a waiver from the requirement if the fire marshal believes the precautions are appropriate and safe
Enhancing Generator Flexibility

## Slide 45: Reporting
Final Rule: Biennial Report (BR) Clarifications Consistent with Existing BR Guidance
Regulations will not list specific data elements to be reported, but instead refer generators directly to the form instructions
LQGs must report all hazardous waste generated and managed on-site in reporting year; LQGs that generate and manage hazardous wastes off-site must follow existing BR guidance
LQGs must report hazardous wastes generated throughout the calendar year, even for months when they are an SQG (§ 262.41)
Closing Regulatory Gap
Recycling facilities that do not have a RCRA storage permit must now report hazardous wastes being recycled
Clarifying Regulations, Strengthening Environmental Protection

## Slide 46: Recordkeeping
Recordkeeping for tanks
Batch process: tank has been emptied every 90 or 180 days
Continuous flow process: document estimated volumes of hazardous waste entering tank daily and exiting the tank within 90 or 180 days of first entering
Clarifying Regulations, Strengthening Environmental Protection

## Slide 47: Reporting and Recordkeeping
EPA is not finalizing on the following that it proposed or took comment on
Maintaining documentation of waste determinations until the facility closes
Notifying the state or EPA of closure of a waste accumulation unit at a facility
Requiring documentation of container weekly inspections
Clarifying Regulations, Strengthening Environmental Protection

## Slide 48: Closure
Final Rule
Require closure as a landfill if LQGs accumulating hazardous wastes in containers fail to clean close
Notification – Closure of waste accumulation area
  Require LQGs to place notice in their operating record within 30 days after closure identifying location of unit within facility; or meet closure performance standards and notify EPA.
Notification – Closure of facility
  Notify EPA or authorized state no later than 30 days prior to closing facility, and
  Notify EPA or authorized state within 90 days after closing facility that it has complied with closure performance standards or notify if it can’t clean close
  LQG can request extension but must notify EPA or authorized state within 75 days after closing facility
Strengthening Environmental Protection

## Slide 49: Major Changes by Generator Category
New Provision | VSQG | SQG | LQG
Reorganization | X | X | X
Consolidation | X |  | X
Episodic | X | X | 
50-foot waiver |  |  | X
Marking and Labeling |  | X | X
Marking RCRA Waste Codes |  | X | X
SQG Re-notification |  | X | 
Quick Reference Guide |  |  | X
Closure |  |  | X
Closure as Landfill if can’t clean close |  |  | X
BR reporting by recyclers who don’t store |  | X | X

## Slide 50: EPA Points of Contact
Kathy Lett
703-605-0761
Lett.Kathy@epa.gov
Mary Beth Sheridan
703-308-4941
Sheridan.MaryBeth@epa.gov
Brian Knieser
703-347-8769
Knieser.Brian@epa.gov